SOCKET COMMUNICATION

---
Introduction to TCP/IP on Cavli Modules
Cavli modules (e.g., C16QS, C1RM) support embedded TCP/IP stacks via AT commands.
These commands allow opening TCP/UDP sockets, sending/receiving data, and managing connections.

---
AT+QIOPEN – Opening a Socket Syntax:
AT+QIOPEN=<cid>,<connID>,"<type>","<remoteIP>",<remotePort>[,<localPort>[,<accessMode>]]
Key Parameters:
cid: PDP context ID (1–16)
connID: Socket ID
type: "TCP", "UDP", "TCP LISTENER", etc.
remoteIP: Target IP or domain
localPort: Port number
accessMode: 0 = buffer, 1 = direct push, 2 = transparent
Example:
AT+QIOPEN=1,0,"TCP","192.168.1.100",5000,0,0
Response:
+QIOPEN: 0,0

---
AT+QISEND – Sending Data Usage in Buffer/Direct Mode:
AT+QISEND=<connID>
Wait for > prompt
Type message
Press Ctrl+Z to send
Example:
AT+QISEND=0
> Hello IoT Server
<Ctrl+Z>
SEND OK

---
Access Modes & Data Flow
Access Modes:
0 = Buffer mode (use QIRD to read)
1 = Direct push mode (URC-based receive)
2 = Transparent mode (streamed like serial)
Reading Data in Buffer Mode:
AT+QIRD=<connID>,<maxLen>

---
Closing and Monitoring Sockets
Close connection: AT+QICLOSE=<connID>
Query socket state: AT+QISTATE? or AT+QISTATE=1,<connID>
Check PDP: AT+CGDCONT?, AT+CGACT?

---
Sample Full TCP Session
AT+CGDCONT=1,"IP","airtelgprs.com“
AT+CGACT=1,1
AT+QIOPEN=1,0,"TCP","203.0.113.5",8080,0,0
+QIOPEN: 0,0
AT+QISEND=0
> Hello from Cavli
<Ctrl+Z>
SEND OK

---
Conclusion
Cavli modules support reliable TCP/UDP communication using standardized AT commands.
AT+QIOPEN is used to open a socket connection.
AT+QISEND is used to transmit data over the established socket.
A typical communication workflow:
Set APN → Activate PDP → Open Socket → Send/Receive → Close Connection
These modules adhere to the 3GPP-standard AT command set, ensuring compatibility and robustness across networks.